## Slide 1
STG17 TECHNICAL WORKSHOP · DAY 4 · AFRICA AFTER DARK
Night-Time Lights
What the darkness tells us — reading Africa’s development from space
Concepts, instruments, artefacts and the workflow behind today’s four laboratories: from raw radiance to a validated subnational indicator.
African Development Bank · African Union — STATAFRIC · National Institute of Statistics of Rwanda
Opening talk · 09:00 – 09:30 · Specialized Technical Group on Emerging Issues (SHaSA II)
Notes: [09:00 · 30 seconds] Welcome to Day 4. Frame the day: this is not a gallery of beautiful pictures of Africa at night. It is a session about a measurement instrument that an NSO can use, test and publish from. This talk is deliberately short — 30 minutes — because the rest of the day is spent in the data. Opening question to the room: "If you could take only one photograph of your country to judge how it is doing, what would you photograph?" The answer this field gives is: photograph it at night. Note: slides marked REFERENCE in these notes are there for the laboratories; skim them live.

## Slide 2
INTRODUCTION · CONTEXT
Why Night-Time Lights at an STG17 workshop?
Night-Time Lights · STG17 Technical Workshop · Day 4
02
A continental mandate
SHaSA II, adopted by the AU Executive Council in January 2018, is the continental strategy for statistics. STG17 is its Specialized Technical Group for emerging issues — big data, open data and, increasingly, AI.
This workshop implements Work Package 4 of the STG17 Action Plan 2025–2030: activity 4.2, project-driven training on emerging technologies.
What countries said in Kigali (Sept 2025)
Satellite and alternative-data experience already exists across Africa, but it is unevenly documented and rarely shared in a form others can reuse. Quality and ethics must stay in view.
What today’s work feeds in the Action Plan
Notebooks, maps and NTL technical note on GitHub
2.1.1
Methodological guidelines for new data sources
Validated steps and limitations statement
4.2.1
Reference manuals on key data skills
Country NTL analysis presented on Day 5
3.1.1 · 3.1.2
Champion-led projects; regional pooling
Source: STG17 Workshop concept note and agenda (V01092026); STG17 Action Plan 2025–2030.
Notes: [1 min] Anchor the session in the institutional context. STG17 is the SHaSA II Specialized Technical Group on emerging issues. At the first Annual Meeting in Kigali (10–12 September 2025) countries said the same thing: experience with satellite and alternative data exists across the continent, but it is unevenly documented and rarely shared in reusable form. Today is designed to fix that for one data source. Stress that what participants build today does not stay in the room: it feeds the Action Plan 2025–2030 — methodological guidelines, reference manuals and the Day 5 country presentations.

## Slide 3
INTRODUCTION · TODAY
Today: from raw pixels to a public indicator
Night-Time Lights · STG17 Technical Workshop · Day 4
03
09:00
Talk
Concepts & utility
Shared vocabulary
09:30
Collect
Access rasters, bands, quality flags; clip to national extent
National subset
10:45
Explore
Distributions, masks, monthly variation; hunt the artefacts
Artefact log
14:00
Analyse
Zonal statistics, time series, change detection, maps
Indicator tables & maps
15:45
Validate
Correlate with official data; decide fitness for use
Evidence + decision
16:30
Publish
Commit notebooks, maps and limitations to GitHub
Day 5 presentation
How this talk is built: every artefact named in Section 5 is one you will look for in your own country’s data at 10:45. The limitations statement you write at 15:45 is part of the deliverable, not a disclaimer.
Notes: [1 min] Show the whole day before the talk begins. Each laboratory produces something concrete, and the chain ends with a public GitHub repository and material for Friday. Point out the logic: we name artefacts in this talk, you HUNT them at 10:45, you COMPUTE at 14:00, and you JUDGE fitness for use at 15:45. The limitations statement is not an afterthought; it is a deliverable.

## Slide 4
INTRODUCTION · ROADMAP
Six questions, thirty minutes
Night-Time Lights · STG17 Technical Workshop · Day 4
04
01
Foundations
Why should a photograph of the dark tell us anything?
02
The instruments
What is measuring, and what can it resolve?
03
From photons to data
How do nights of observations become a number?
04
Applications
Which statistical questions can lights answer?
05
Limits
Where does the inference break, and how would you know?
06
From talk to lab
How do we do this well, starting at 09:30?
BY THE END OF THIS TALK YOU CAN
Explain what a night-lights pixel measures — and what it does not
Choose a product (daily, monthly, annual) that fits a statistical question
Recognise the six artefacts you will hunt in your own data this morning
Notes: [30 sec] Give the map before the territory. Each section answers one question. Section 5 (Limits) is not an afterthought: it is where most of the intellectual content of the field sits, and it drives this morning's laboratory. Read the three learning objectives aloud.

## Slide 5
SECTION 1
01
Foundations
Why should a photograph of the dark tell us anything at all?
The core idea · Definitions · The inferential chain
Notes: [Section 1 · ~5 min] Transition. We start with the physical idea, then define the object precisely, then show the chain of assumptions that every study depends on.

## Slide 6
01 · FOUNDATIONS · THE CORE IDEA
Light is what human activity leaks
Night-Time Lights · STG17 Technical Workshop · Day 4
06
Almost everything people do after sunset requires light — and part of that light escapes upward, into the field of view of a satellite.
That physical fact turns the night side of the planet into an observation of human presence that no census, survey or administrative register can match on all four properties at once:
Globally consistent
Same method in every country
Spatially continuous
Every ≈500 m grid cell
Politically neutral
Independent of reporting
Freely available
Open NASA / EOG products
1992
Start of the continuous digital DMSP record — three decades of history
742 m
VIIRS Day/Night Band pixel, nearly constant across the swath
Nightly
Global VIIRS overpass around 01:30 local time, since 2012
For an NSO: censuses come roughly once a decade, surveys every few years — lights arrive every night, for every district.
Notes: [1.5 min] This is the conceptual hinge of the talk. Almost everything people do after sunset needs light, and a fraction escapes upward. That single fact gives a measurement with four properties no census, survey or register has at the same time: globally consistent, spatially continuous, politically neutral, and freely available. The word "leaks" is deliberate: we observe waste light, not activity itself — plant that seed of scepticism now. For NSOs, the key comparison is frequency and granularity: a census roughly every ten years, household surveys every few years, lights every night for every half-kilometre.

## Slide 7
01 · FOUNDATIONS · DEFINITIONS
What night-time lights are — and are not
Night-Time Lights · STG17 Technical Workshop · Day 4
07
WORKING DEFINITION
Night-time lights (NTL) are measurements of visible and near-infrared radiance travelling upward from the Earth’s surface, recorded by a satellite sensor during local night, when the scene is free of direct sunlight.
What it is
A physical measurement
Radiance in nW·cm⁻²·sr⁻¹ for calibrated sensors (VIIRS).
A consistent grid
Same method over every country — Rwanda and Nigeria alike.
A near-real-time record
Daily since 2012; monthly and annual composites, free of charge.
What it is not
A photograph
The familiar “Earth at night” is a statistical composite of many cloud-free nights.
A direct measure of people or income
Those are inferences — each needs its own justification.
A complete record of lighting
Indoor, shielded and sideways light never reaches the sensor.
Notes: [1 min] Read the working definition once. Then dwell on the right-hand column. The most common error in applied work is treating the composite as a picture and reasoning about it visually rather than radiometrically. The second is jumping from radiance to population or income without justifying the link. Units matter: nanowatts per square centimetre per steradian — you will see them in the HDF files at 09:30.

## Slide 8
01 · FOUNDATIONS · THE INFERENTIAL CHAIN
From electricity to a pixel value: five links
Night-Time Lights · STG17 Technical Workshop · Day 4
08
1
Energy & infrastructure
A grid, generator or fuel supply exists and is operating.
2
Activity after dark
People use that energy for lighting: streets, homes, markets, industry.
3
Upward emission
A fraction of the light escapes upward rather than being shielded.
4
Atmospheric transfer
Photons cross the atmosphere, attenuated by aerosols, vapour and cloud.
5
Sensor response
The detector integrates them over its band into a radiance value.
Where the chain breaks in African contexts — a dark pixel can mean …
Link 1
Load-shedding or fuel shortage — people are there, power is not
Link 2–3
Solar lanterns and small home systems too faint to detect
Link 4
Rainy-season cloud, harmattan dust, biomass-burning smoke
Link 5
Rural light below the sensor’s detection floor
Notes: [1.5 min] Walk the chain forwards, then backwards. Backwards is the diagnostic exercise: given a dark pixel in your country, list every link that could have produced it. The bottom panel gives African-context examples for each link: load-shedding breaks link 1; low-power solar lanterns may not produce enough upward light to cross the detection floor; rainy-season cloud and dry-season dust or biomass-burning smoke attenuate link 4. Participants should be able to generate at least five distinct explanations for darkness. This is exactly the reasoning required in the validation lab this afternoon.

## Slide 9
SECTION 2
02
The instruments
What exactly is doing the measuring, and what can it resolve?
History · DMSP versus VIIRS · Saturation and dynamic range
Notes: [Section 2 · ~4 min] The choice of sensor determines which questions are answerable. Keep this section brisk.

## Slide 10
02 · THE INSTRUMENTS · HISTORY
Fifty years of looking down at the dark
Night-Time Lights · STG17 Technical Workshop · Day 4
10
1970s
DMSP-OLS night imagery (film). City lights noticed as a by-product of cloud detection.
1992
Start of the digital DMSP archive → “stable lights” annual series to 2013.
2011
Suomi NPP launched with VIIRS: first sensor calibrated for night-time radiance.
2012
VIIRS monthly cloud-free composites; NASA Black Marble record begins (Jan 2012).
2017
NOAA-20 launched with a second VIIRS; Black Marble twin products from 2018.
2018
Luojia-1-01 demonstrates ≈130 m night imaging from a small satellite.
2021
SDGSAT-1 Glimmer imager: colour night imagery at 10–40 m.
2022
NOAA-21 launched: a third VIIRS extends the record into the 2030s.
The irony: the first instrument was built to see moonlit clouds. City lights were noise — it took two decades for anyone to treat the noise as the signal.
Notes: [1 min] The historical irony is worth saying aloud: DMSP was built to see clouds by moonlight for military weather forecasting. City lights were noise; it took two decades before anyone treated that noise as the signal. Key message for continuity: VIIRS now flies on three satellites (Suomi NPP, NOAA-20, NOAA-21), so an NSO investing in NTL methods today is investing in a data stream with a future. Black Marble products are produced for both Suomi NPP (VNP46) and NOAA-20 (VJ146).

## Slide 11
02 · THE INSTRUMENTS · SENSOR COMPARISON
Two sensors, two different sciences
Night-Time Lights · STG17 Technical Workshop · Day 4
11
DMSP-OLS · historical
VIIRS Day/Night Band · modern
Period
1992 – 2013 (archive)
2012 – present (standard)
Radiometry
6-bit digital numbers 0–63, no on-board calibration
14-bit, calibrated radiance in nW·cm⁻²·sr⁻¹
Resolution
≈2.7 km, gridded at 30 arc-seconds (≈1 km)
742 m, nearly constant across the swath
Saturation
City cores clip at 63
Wide dynamic range, three gain stages
Sensitivity
Misses faint, rural lighting
Detects far fainter light than DMSP
Products
Annual composites only
Daily, monthly and annual — open licence
Next generation: Luojia-1-01 (≈130 m), SDGSAT-1 Glimmer (10 m panchromatic, 40 m colour) and commercial constellations resolve streets and distinguish lamp types by colour.
Notes: [1.5 min] Teaching point: DMSP gives a long history but crude, saturated, uncalibrated values; VIIRS gives precision but only since 2012. Any long-run series for your country needs both, and therefore an explicit harmonisation step — this is the "sensor discontinuity" artefact you will meet later. Mention that the next generation (SDGSAT-1, Luojia, commercial) adds colour, the dimension both legacy sensors lack.

## Slide 12
02 · THE INSTRUMENTS · DYNAMIC RANGE
Why the brightest places say the least
Night-Time Lights · STG17 Technical Workshop · Day 4
12
DMSP returns 63 above a certain brightness — a suburb and a downtown core look identical.
VIIRS spans roughly seven orders of magnitude, with three switchable gain stages.
Its low noise floor makes a single lit fishing boat visible on a dark lake or ocean.
Read this before you regress
Saturation is a ceiling, not noise you can average away. The information was never recorded — correcting it means modelling what the sensor failed to see.
Chart: Sensor response as surface brightness rises (schematic)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
DMSP-OLS (6-bit) | 18 | 36 | 55 | 73 | 91 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
VIIRS DNB (14-bit) | 7 | 14 | 21 | 29 | 36 | 43 | 50 | 57 | 64 | 71 | 79 | 86 | 93 | 100
Schematic illustration — not fitted data. VIIRS range per Elvidge et al. (2017).
Notes: [1 min] The clearest analogy: imagine a thermometer that only reads "40°C or more". You can still study cold places with it, but every question about heat becomes a question about your model rather than your data. That is DMSP for city centres such as Lagos, Cairo or Johannesburg. VIIRS was designed around that limit: its Day/Night Band spans about seven orders of magnitude using three gain stages. The chart is schematic — not fitted data. For Africa, the opposite end of the range matters just as much: most rural settlements sit near the detection floor, which is why sensitivity matters more to us than saturation.

## Slide 13
SECTION 3
03
From photons to data
How does a night of observations become a number you can publish?
Processing · Products · What glows · Indicators · Example
Notes: [Section 3 · ~7 min] This is the section closest to the laboratories. Slides 15 and 17 are the ones participants will return to during the day.

## Slide 14
03 · FROM PHOTONS TO DATA · METHOD
How a night-lights image is manufactured
Night-Time Lights · STG17 Technical Workshop · Day 4
14
1
Screen for cloud
Only nights flagged cloud-free enter a composite. In the wet tropics most nights may be discarded.
2
Remove sunlight
Twilight, glint and instrument stray light are corrected or excluded.
3
Correct for the Moon
Moonlight reflected by the ground mimics emitted light; it is modelled out.
4
Filter transients
Fires, lightning, aurora and moving boats are flagged by their instability.
5
Composite & tile
Surviving nights are averaged into a monthly or annual grid, tiled globally.
You will see these steps as layers at 09:30
Black Marble VNP46A2 carries the corrected radiance plus its evidence: cloud-mask flag, lunar irradiance, snow flag and a Mandatory_Quality_Flag (0 = high quality; 1–5 = poor, incl. aurora and glint).
A product, not a snapshot
Two products for the same month can legitimately differ. Always record product and version.
Sources: Román et al. (2018); NASA LAADS DAAC VNP46A2 v2 product page.
Notes: [1.5 min] Stress step 1 for our continent. Cloud screening is why the Congo Basin and coastal West Africa have far fewer usable observations than the Sahara or the Kalahari — a systematic geographic bias in any cross-country comparison. Ask: does fewer observations bias the result, or merely widen the error bars? In the 09:30 lab you will see each of these steps as a layer in the file: the cloud mask flag, the lunar irradiance, the snow flag and the Mandatory_Quality_Flag, where 0 means high quality. The image is a statistical product, not a snapshot — two products for the same month can legitimately differ.

## Slide 15
03 · FROM PHOTONS TO DATA · PRODUCTS · FOR THE 09:30 LAB
The NASA Black Marble product family
Night-Time Lights · STG17 Technical Workshop · Day 4
15
Content
Corrections
Typical use
VNP46A1
DAILY
At-sensor radiance (top of atmosphere)
Uncorrected — inputs & geometry only
Advanced users
VNP46A2
DAILY
Moonlight-adjusted, gap-filled NTL
Cloud, lunar, atmosphere, terrain, stray light
Blackouts, reliability, events
VNP46A3
MONTHLY
Composite of corrected daily NTL
As A2, plus number of observations & quality
Programme evaluation, seasonality
VNP46A4
ANNUAL
Composite of corrected daily NTL
As A2, plus number of observations & quality
Long-run trends, subnational panels
Common to all: 15 arc-second grid (≈500 m at the equator) · 10°×10° tiles · HDF-EOS5 · from January 2012 · NOAA-20 twins named VJ146*.
Gotcha: radiance is stored as integers — multiply by the 0.1 scale factor and mask the 65535 fill value. Alternatives: EOG VIIRS Nighttime Lights (VNL) composites; Google Earth Engine catalogue.
Notes: [1 min live — REFERENCE slide for the 09:30 lab] Four products. A1 is uncorrected top-of-atmosphere radiance: do not use it for statistics without doing the corrections yourself. A2 is the daily corrected product — the basis of everything else. A3 and A4 are monthly and annual composites built from the daily inputs. All share a 15 arc-second grid (about 500 m at the equator), 10°×10° tiles, HDF-EOS5 format, and a record from January 2012. Practical gotchas for the lab: the radiance layer is stored as an unsigned integer with a scale factor of 0.1 and a fill value of 65535 — forget either and your numbers are wrong by a factor of ten or contaminated by fill values. NOAA-20 twins carry the VJ146 prefix. Earth Observation Group (Colorado School of Mines) VNL annual and monthly composites and Google Earth Engine are the two main alternatives.

## Slide 16
03 · FROM PHOTONS TO DATA · INTERPRETATION
What actually glows over Africa at night
Night-Time Lights · STG17 Technical Workshop · Day 4
16
Cities & settlements
SIGNAL
Streets, buildings, markets, vehicles. The dominant and most-studied part of the signal.
Corridors, ports & mines
SIGNAL
Highways, ports, airports, mining and industrial sites: the network between the bright spots.
Gas flares
MASK
Very bright, isolated points in oil & gas regions — e.g. the Niger Delta, Algeria, Libya. Mask them.
Fishing lights
CONTEXT
Lamp-attraction fishing on Lake Victoria and Lake Tanganyika; offshore fleets.
Fires
MASK
Savanna and agricultural burning: intense, short-lived and strongly seasonal.
Natural & reflected light
REMOVE
Moonlight on bright desert sand or salt pans, airglow. Not a human signal at all.
Gas flares are catalogued separately by the VIIRS Nightfire product (Earth Observation Group).
Notes: [1 min] This slide prevents the most embarrassing class of error: reporting a booming economy in an oil-producing region when what changed was flaring, or a surge of activity in the middle of Lake Victoria that is actually a fishing fleet. Only one of these six sources is usually the signal an NSO wants. Always look at the map before trusting the number — which is exactly what the Explore lab is for.

## Slide 17
03 · FROM PHOTONS TO DATA · INDICATORS · FOR THE 14:00 LAB
Turning an image into a number
Night-Time Lights · STG17 Technical Workshop · Day 4
17
Toy district · radiance per pixel
0.1
0.3
0.2
0.0
0.4
2.5
6.0
0.6
0.2
4.0
12.0
1.5
0.0
0.8
1.2
0.3
Shaded = above threshold 0.5 nW·cm⁻²·sr⁻¹
30.1
Sum of Lights (SOL)
Total radiance inside a boundary. Workhorse of the economics literature; most sensitive to background noise.
8 px
Lit area
Pixels above a chosen threshold. Intuitive — but the threshold is a researcher choice.
3.6
Mean radiance (lit)
Brightness independent of extent. Separates a district getting brighter from one getting bigger.
Raise the threshold to 1.0 → lit area falls from 8 to 6 pixels (−25%). Always report product, version, boundary, threshold and masks — and test the threshold.
Illustrative values. Light concentration (Gini of radiance) is a fourth family, used for spatial inequality.
Notes: [1.5 min] Work the toy example live — it is the fastest way to make the three indicators concrete. A 4×4 district of pixels, radiance in nW·cm⁻²·sr⁻¹. Sum of Lights adds everything: 30.1. Lit area counts pixels above the threshold: with 0.5 we get 8 pixels. Mean radiance over lit pixels is 28.6 / 8 = 3.6. Now raise the threshold to 1.0: lit area drops from 8 to 6 pixels — a 25% change produced by a choice, not by the world. That is why the threshold must be reported and tested. Sum of Lights is sensitive to background noise because every faint pixel contributes. Mean radiance separates a district getting brighter from one getting bigger. A fourth family — concentration or Gini of light — is used as a spatial inequality proxy.

## Slide 18
03 · FROM PHOTONS TO DATA · WORKED EXAMPLE
One question, end to end
Night-Time Lights · STG17 Technical Workshop · Day 4
18
Did the 2023 mini-grid programme actually bring light to its target villages?
1
State the claim in light terms
Electrified villages should show more nights above their background radiance after commissioning.
2
Choose the product
VNP46A3 monthly to date the change; VNP46A2 daily if you also want reliability. Record the version.
3
Define the units
Settlement footprints plus a small buffer — not whole districts, where a few lit villages vanish.
4
Pick indicator & control
Mean radiance and share of lit nights; controls = similar villages outside the programme.
5
Read the difference
A step change in programme villages that is absent in controls is evidence; a common rise is regional.
6
Try to break it
Check fires, flares, moon and season; compare with utility connection or programme monitoring records.
Notes: [1.5 min] Walk this slowly — it is the slide people will reuse. The question is typical of what a ministry might ask an NSO. Step 3 matters in rural Africa: if you average over a whole district, a few newly lit villages disappear into the dark background, so use settlement footprints. Step 4 — the control group of comparable villages outside the programme — is what turns a description into evidence, and it costs almost nothing. Step 6 is where most published work is thinnest: try to break your own result before someone else does.

## Slide 19
SECTION 4
04
Applications
Which statistical questions can this data actually answer?
SDG map · Economy · Energy access · Urbanisation · Crises
Notes: [Section 4 · ~6 min] For each application, keep asking: what would have to be true about lighting behaviour for this inference to hold?

## Slide 20
04 · APPLICATIONS · OVERVIEW
Where lights can support SDG monitoring
Night-Time Lights · STG17 Technical Workshop · Day 4
20
SDG 1
Poverty & wealth mapping
Small-area estimates combining lights with survey data
SDG 7
Electricity access & reliability
Locate unserved settlements; track how often lights are on
SDG 8
Economic activity
Subnational GDP downscaling; short-term activity signals
SDG 9
Infrastructure
Corridors, ports, industrial and special economic zones
SDG 11
Urbanisation
Urban extent, sprawl versus densification, new towns
SDG 16 · humanitarian
Conflict & disasters
Blackouts, displacement signals, recovery tracking
A complement, not a replacement. Lights add spatial detail, frequency and independent verification to official statistics — they do not replace the census or the survey.
Notes: [1 min] A map of uses, framed by the SDGs an NSO already reports on. The key phrase is "support": night lights are a complement to official statistics, useful for disaggregation, nowcasting and verification, never a replacement for the survey or the census. Invite participants to pick the one row most relevant to their office — that is the question to carry into this afternoon's analysis.

## Slide 21
04 · APPLICATIONS · APPLICATION 01
Measuring the economy from orbit
Night-Time Lights · STG17 Technical Workshop · Day 4
21
What the evidence shows
Henderson, Storeygard & Weil (2012)
Lights carry real information on economic growth and can improve GDP estimates where national accounts are weak.
Bruederle & Hodler (2018)
Lights track household wealth, education and health at the local level, using DHS survey clusters in Africa.
Martinez (2022)
Lights used as an independent benchmark to test the credibility of reported GDP growth.
Why the lights–output link is not stable
Sector mix: agriculture and mining create value with little light
Income level: bright cores saturate or plateau
Lighting technology: LED retrofits change light per watt
Power supply: load-shedding dims lights, not output
WHERE LIGHTS HELP MOST
Subnational
High-frequency
Informal economy
Sources: Henderson et al. (2012) AER 102(2); Bruederle & Hodler (2018) PLOS ONE 13(9); Martinez (2022) JPE 130(10).
Notes: [1.5 min] The honest version: night lights are a poor substitute for good national accounts and an excellent complement to weak or coarse ones. Henderson, Storeygard and Weil (2012) showed lights carry real information on growth. Bruederle and Hodler (2018) linked lights to household-level development indicators from DHS surveys at the local level in Africa. Martinez (2022) used lights as an independent benchmark for reported GDP growth — a reminder that NTL is also a credibility tool for official statistics. The elasticity of lights to output is neither one nor stable: agriculture and mining generate much value with little light, which matters for most African economies. Lights help most where statistics are coarsest: subnational, high-frequency and informal.

## Slide 22
04 · APPLICATIONS · APPLICATION 02
Energy access and SDG 7: Africa’s defining gap
Night-Time Lights · STG17 Technical Workshop · Day 4
22
655 M
people without electricity worldwide (2024)
> 560 M
of them in sub-Saharan Africa
Chart: Rural sub-Saharan Africa without electricity (millions)
| 2010 | 2024
Rural SSA without electricity (millions) | 376 | 447
Locate the unserved
Settlements visible by day but dark at night are candidate unelectrified communities.
Verify programmes
A grid extension that produces no new light has not, in a meaningful sense, been delivered.
Measure reliability
Daily data reveal how often lights are on — load-shedding a binary “connected” statistic hides.
Plan the last mile
Distance to lit corridors informs grid extension vs mini-grid vs stand-alone solar.
Mission 300 (World Bank Group & AfDB): 300 M people connected by 2030 — monitoring at that scale needs spatial evidence.
Sources: Tracking SDG 7: The Energy Progress Report (IEA, IRENA, UN DESA, World Bank, WHO), 24 June 2026; HREA, Min & O’Keeffe (Univ. of Michigan).
Notes: [1.5 min] The Tracking SDG 7 report released on 24 June 2026 puts the global access deficit at 655 million people in 2024, with more than 560 million in sub-Saharan Africa. The rural deficit in the region grew from 376 million in 2010 to 447 million in 2024 — population growth has outpaced connections. Mission 300, led by the World Bank Group and the African Development Bank, aims to connect 300 million Africans by 2030; programmes of that scale need independent, spatially detailed monitoring. The surprising point: reliability. Official statistics record a household as connected whether it has power four hours a day or twenty-four. Nightly VIIRS observations can tell the difference. The High Resolution Electricity Access (HREA) dataset from the University of Michigan and the World Bank already estimates settlement-level electrification likelihood from nightly VIIRS data.

## Slide 23
04 · APPLICATIONS · APPLICATION 03
Urbanisation and the shape of a city
Night-Time Lights · STG17 Technical Workshop · Day 4
23
Sprawl
Footprint expands outward at low intensity
Lit area +40% · Radiance +6%
Densification
The same footprint intensifies
Lit area +6% · Radiance +40%
Same Sum of Lights — two very different cities (illustrative).
Map the footprint where registers are missing
Lights reveal built-up extent where cadastral records or recent maps do not exist.
Separate sprawl from densification
Compare growth in lit area with growth in radiance — it matters for transport and services.
Detect new towns early
Mining boomtowns, economic zones and displacement settlements appear before official geography.
Pair with population grids
Use WorldPop or GHSL — bright pixels are not people.
Notes: [1 min] Africa is urbanising fast, and cadastral records rarely keep up. The sprawl-versus-densification diagnostic is the most transferable idea here: it needs two indicators, not one — which is exactly why Sum of Lights alone is insufficient for urban work. The two illustrative cities have the same total light but completely different policy implications for transport, services and emissions. Always pair lights with population and built-up grids: bright pixels are not people, and an empty lit highway proves it.

## Slide 24
04 · APPLICATIONS · APPLICATION 04
When the lights go out: conflict and disaster
Night-Time Lights · STG17 Technical Workshop · Day 4
24
Conflict · Sudan, 2023
After fighting began in Khartoum in April 2023, the capital’s lights fell to the noise level by May (EOG). UNOSAT mapped power outages from NTL in June 2023.
Conflict · Syria, 2011–2014
Li & Li (2014) measured a loss of more than 70% of night-time light nationally, with losses tracking displacement province by province.
Disaster · Puerto Rico, 2017
After Hurricane Maria, NASA Black Marble daily data mapped the blackout and tracked restoration neighbourhood by neighbourhood.
The interpretive rule: absence of light is not absence of people
Darkness may mean displacement, destruction, fuel shortage, curfew, a grid failure — or a decision to switch off street lights. The satellite cannot tell which. Corroboration with ground information is not optional, and uncertainty must be stated.
Sources: Payne Institute / EOG (Sept 2024); UNOSAT (June 2023); Li & Li (2014) IJRS 35(18); Román et al. (2019) on Puerto Rico.
Notes: [1.5 min] The most ethically loaded application in the deck. Sudan is the African case: after fighting broke out in Khartoum on 15 April 2023, the Earth Observation Group reported that by May 2023 the capital's lights had dimmed to the noise level, and UNOSAT published a power-outage assessment from night-time imagery in June 2023. Syria (Li and Li, 2014) and Puerto Rico after Hurricane Maria (Black Marble daily products) are the reference studies. Night lights are used in humanitarian and human-rights reporting, so errors have consequences: insist on triangulation with ground information and honest statements of uncertainty. For NSOs, the value is rapid situational evidence when field collection is impossible.

## Slide 25
SECTION 5
05
Limits
Where does the inference break — and how would you know?
Six artefacts to hunt · What the satellite cannot see
Notes: [Section 5 · ~4 min] This section is the brief for the 10:45 Explore lab. Name each artefact; participants will find them in their own rasters.

## Slide 26
05 · LIMITS · YOUR BRIEF FOR 10:45
Six artefacts you will hunt this morning
Night-Time Lights · STG17 Technical Workshop · Day 4
26
Blooming / overglow
Light spills beyond settlement edges; lit area inflated, most for small towns.
Spot it: Compare lit extent with a built-up layer; profile across a city edge.
Saturation
Flat-topped city cores in DMSP (value 63); no variation where activity peaks.
Spot it: Histogram spike at the maximum value in any DMSP-based series.
Gas flares
Extremely bright isolated points in oil and gas regions.
Spot it: Overlay VIIRS Nightfire flare sites; mask before summing.
Seasonality
Regular annual cycle from cloud, vegetation, fires, festivities.
Spot it: Plot the monthly series; check the number-of-observations layer.
Sensor discontinuity
Jumps at DMSP→VIIRS (2012–13), satellite or product-version changes.
Spot it: Never splice raw series; check version metadata; use a documented harmonisation.
Rural low-light noise
Faint values near the detection floor that flicker from month to month.
Spot it: Compare with uninhabited pixels nearby; test several thresholds.
Harmonised DMSP–VIIRS series exist (e.g. Li et al., 2020, Scientific Data) — use them with their documented assumptions.
Notes: [2 min] These six are named exactly as in the agenda for Hands-on part 2. For each: what it looks like, and the quickest way to spot it. Blooming is the most under-appreciated: lit area is almost always overestimated, and the bias is proportionally larger for small towns than big cities — which distorts exactly the rural–urban comparisons development work depends on. Sensor discontinuity is the classic trap for long series: never splice DMSP and VIIRS raw values; the same applies to product version changes. Ask each team to keep an artefact log: which ones are present in your country, where, and what you did about them.

## Slide 27
05 · LIMITS · THE BLIND SPOTS
What the satellite cannot see
Night-Time Lights · STG17 Technical Workshop · Day 4
27
Off-grid & low-power light
Solar lanterns and small home systems may sit below the detection floor — electrified, yet dark from orbit.
One moment per night
An overpass near 01:30 misses evening markets, early shifts and daytime economic activity.
No blue, no colour
The Day/Night Band (≈500–900 nm) barely sees white-LED blue: an LED retrofit can look darker from space.
Persistent cloud
Long rainy seasons leave few valid nights; monthly values may rest on a handful of observations.
EVIDENCE · URBAN BIAS
Sudan: who can be monitored?
Before the 2023 war, settlements near Khartoum were far more likely to be monitorable with NTL. In West and South Darfur, only settlements close to district capitals had enough baseline light.
9.6%/yr
sky brightening seen from the ground (2011–22)
2.2%/yr
lit-area growth seen from space (2012–16)
Sources: Humanities & Social Sciences Communications (2025), “The rural limits of conflict monitoring using nighttime lights”; Kyba et al. (2017, 2023).
Notes: [2 min] Four blind spots that matter particularly in Africa. Off-grid: millions of households rely on solar lanterns or small home systems that emit too little upward light to be detected — they are "electrified" in the SDG 7 sense but may look dark. Timing: a single overpass around 01:30 misses evening markets and activity before midnight. Colour: the Day/Night Band responds roughly from 500 to 900 nm and barely sees the blue emission of white LEDs, so a city that converts to LEDs can look darker from orbit while getting brighter to the eye; ground citizen-science data show the sky brightening much faster (9.6% per year, 2011–2022) than satellites show lit area growing (2.2% per year, 2012–2016). Cloud: persistent rainy seasons leave few valid observations. The right-hand panel is the strongest African evidence of urban bias: a 2025 study of Sudan showed that in West and South Darfur only settlements close to district capitals had enough baseline light to be monitored at all.

## Slide 28
SECTION 6
06
From talk to lab
How do we do this well — starting at 09:30?
Workflow · Choosing a product · Validation · Checklist · Discussion
Notes: [Section 6 · ~4 min] The bridge to the laboratories. Slides 29–32 are reference material for the rest of the day.

## Slide 29
06 · FROM TALK TO LAB · TODAY’S WORKFLOW
Five stages, one reproducible pipeline
Night-Time Lights · STG17 Technical Workshop · Day 4
29
Collect
09:30
NASA Earthdata / LAADS DAAC
EOG VNL · Google Earth Engine
Bands & quality flags
National subset
Explore
10:45
Histograms & maps
Cloud & quality masks
Month-to-month variation
Artefact log
Analyse
14:00
Zonal stats by admin level
Annual & monthly series
Change detection
Tables & maps
Validate
15:45
Official subnational data
Population, electrification
Fitness-for-use decision
Evidence + decision
Publish
16:30
Notebooks & maps
Limitations statement
README: method, sources, licence
Public repository
Example open-source stack: rasterio / xarray (read), geopandas (boundaries), rasterstats or exactextract (zonal statistics), matplotlib (maps).
Notes: [1 min] The day's pipeline in one picture. Each stage has a data source or tool and a concrete output that feeds the next. The Python libraries listed are examples of common open-source options, not requirements. Emphasise reproducibility: every stage ends in a file committed to GitHub, so that another country — or your own office next year — can re-run it.

## Slide 30
06 · FROM TALK TO LAB · CHOOSING A PRODUCT
Which cadence for which question?
Night-Time Lights · STG17 Technical Workshop · Day 4
30
Annual
VNP46A4 · EOG VNL annual
STRENGTH
Cleanest series; noise and ephemeral lights largely filtered.
WATCH OUT FOR
A change cannot be dated within the year.
TYPICAL NSO USE
Subnational panels, long-run trends, urban expansion, poverty mapping.
Monthly
VNP46A3 · EOG VNL monthly
STRENGTH
Dates a change to within a season.
WATCH OUT FOR
Rainy-season months may rest on very few valid nights.
TYPICAL NSO USE
Programme evaluation, seasonal activity, conflict & recovery timelines.
Daily
VNP46A2
STRENGTH
Every night, corrected for moon, atmosphere and terrain.
WATCH OUT FOR
Large volumes; a single night is noisy — aggregate first.
TYPICAL NSO USE
Blackouts, disaster response, reliability of electricity supply.
Rule of thumb: start annual. The finer the cadence, the more corrections you must trust and the more noise you must handle.
Notes: [1 min — REFERENCE] The instinct to reach for daily data is almost always wrong at the start of a project. Annual composites answer most statistical questions with a fraction of the processing burden, and they fail loudly rather than quietly. Move to monthly or daily only when you can say precisely what temporal resolution your question needs — for example, dating the start of a conflict, or measuring reliability of supply.

## Slide 31
06 · FROM TALK TO LAB · VALIDATION · FOR THE 15:45 LAB
Publish, or keep as a diagnostic?
Night-Time Lights · STG17 Technical Workshop · Day 4
31
Q1
Is the relationship strong and stable across units and years?
Set your bar before you look.
Q2
Are artefacts identified and treated?
Flares, blooming, seasonality, noise.
Q3
Is the benchmark independent?
WorldPop uses NTL as a covariate — circular.
All three: yes → Experimental statistic — publish with limitations
Partly → Diagnostic tool — internal use only
No → Not fit for purpose — document why
Limitations statement — template
Part of the deliverable, committed to GitHub
Data
Product, collection version, period, cadence
Choices
Boundaries, radiance threshold, masks applied
Artefacts
Which of the six were found, where, and how treated
Validation
Benchmark, year, number of units, strength of relationship
Decision
Experimental, diagnostic or not fit — and why
Must not be used for
e.g. household income, small-settlement counts
Suggested guide — adapt to your national quality assurance framework. Circularity: see Falchetta et al. (2019), Scientific Data.
Notes: [1 min — REFERENCE for 15:45] A suggested decision guide, to be adapted to your office's own quality assurance framework. Three questions. First, set the bar BEFORE you look at the result: what correlation and stability would you require? Second, have the artefacts been identified and treated? Third — the trap specific to this week — is your benchmark independent? WorldPop population models use night-time lights as one of their covariates, so correlating NTL with WorldPop partly correlates NTL with itself. Prefer census or survey benchmarks for validation. The outcome is one of three decisions, and the limitations statement on the right is part of the deliverable whichever you choose.

## Slide 32
06 · FROM TALK TO LAB · GOOD PRACTICE
A checklist for defensible analysis
Night-Time Lights · STG17 Technical Workshop · Day 4
32
1
Name product and version
VNP46A4 v2, VNL V2.x — they are not interchangeable.
2
Never splice sensors naively
Any DMSP–VIIRS series needs documented harmonisation.
3
Report and test the threshold
Show the finding survives a reasonable range.
4
Mask what you are not studying
Background noise, gas flares, fishing lights, fires.
5
Normalise deliberately
Per capita, per km², or neither — state and defend it.
6
Validate against the ground
Census, surveys, utility records — independent sources.
7
Prefer changes to levels
Differences cancel much of the calibration error.
8
Publish code and limitations
README with method, sources, licence and caveats.
THE GOLDEN RULE
State, in one sentence, what would have to be true about lighting behaviour for your conclusion to hold.
If you cannot write that sentence, you do not yet have a result.
Share it: a documented, reusable repository is how your office contributes to the STG17 methodological guideline on new data sources.
Notes: [30 sec — REFERENCE] Keep this open during the labs. Item 7 is the practical heart of the list: most credible work identifies effects from changes within the same unit over time rather than from cross-sectional levels, because calibration problems largely cancel out. The golden rule is the test for Friday's presentations.

## Slide 33
06 · FROM TALK TO LAB · OVER TO YOU
Three questions worth arguing about
Night-Time Lights · STG17 Technical Workshop · Day 4
33
1
The contradictory region
A region’s Sum of Lights falls 12% in a year while its estimated GDP grows 3%. Give four explanations consistent with both facts — then name the one observation that best discriminates between them.
2
One indicator only
You must monitor a five-year rural electrification programme with one indicator: lit area, Sum of Lights, or the share of nights a settlement is lit. Choose — and defend it against the other two.
3
Publish or not?
Your NTL–electrification relationship is strong in the capital region but weak elsewhere. What do you publish, for which areas, and what goes in your limitations statement?
Format: 5 minutes in country teams, one question each, one spokesperson. Question 3 is the one you will face at 15:45 — keep your answer for the limitations statement.
Notes: [Use during the Explore lab wrap-up or at 15:45 if time is short now] Question 1 rewards the inferential chain: displacement, load-shedding, lamp conversion, flaring changes, and a boundary or product-version change are all live candidates. Question 2 has no single right answer; the best defences mention detection floors and reliability. Question 3 is the one participants will actually face this afternoon — there is no clean answer from satellite data alone, which is the point.

## Slide 34
IN CLOSING
Five things to take into the lab
1
Night lights are a proxy, never the quantity of interest — name the assumption that links them to your question.
2
The instrument defines the science: DMSP saturates, VIIRS calibrates, and neither sees blue light.
3
The data is most valuable where official statistics are thinnest: subnational, high-frequency, in crises and informal economies.
4
Darkness is not emptiness — off-grid light, cloud and load-shedding all look alike from orbit.
5
Validate against independent sources, and publish your limitations with your results.
The darkness tells us a great deal. It does not tell us everything — and it never speaks unprompted.
Notes: [30 sec] Land on the last line. Extracting the signal is now routine and largely automated; the discipline is in knowing what the signal is entitled to mean. Then hand over to the Collect laboratory at 09:30.

## Slide 35
APPENDIX · GLOSSARY
The vocabulary you will meet today
Night-Time Lights · STG17 Technical Workshop · Day 4
35
Radiance
Energy leaving a surface per unit area and solid angle; for NTL in nW·cm⁻²·sr⁻¹.
Digital number (DN)
Uncalibrated sensor count with no physical unit; DMSP reports 0–63.
Composite
Grid assembled from many cloud-free nights — not a photograph of one night.
Stable lights
Product with fires, aurora and other unstable sources removed.
Sum of Lights (SOL)
Total radiance summed over all pixels inside a boundary.
Blooming / overglow
Apparent spread of light beyond its source (scattering, geolocation error).
BRDF correction
Adjustment for how reflected (moon)light varies with viewing and lighting angles.
Zonal statistics
Summary of raster values (sum, mean, count) within each polygon.
Nadir
Point directly beneath the satellite, where the pixel footprint is smallest.
Skyglow
Diffuse brightening of the night sky by artificial light scattered in the atmosphere.
Notes: REFERENCE — hand out rather than read. The two terms that cause most confusion in practice: composite (people keep treating it as a photograph) and digital number (people keep treating it as a physical quantity).

## Slide 36
APPENDIX · SOURCES
Selected references and data sources
Night-Time Lights · STG17 Technical Workshop · Day 4
36
Bruederle, A. & Hodler, R. (2018). Nighttime lights as a proxy for human development at the local level. PLOS ONE, 13(9).
Elvidge, C. D. et al. (2017). VIIRS night-time lights. International Journal of Remote Sensing, 38(21).
Falchetta, G. et al. (2019). A high-resolution gridded dataset to assess electrification in sub-Saharan Africa. Scientific Data, 6.
Henderson, J. V., Storeygard, A. & Weil, D. N. (2012). Measuring economic growth from outer space. American Economic Review, 102(2).
Kyba, C. et al. (2017). Artificially lit surface of Earth at night increasing in radiance and extent. Science Advances, 3(11).
Kyba, C. et al. (2023). Citizen scientists report global rapid reductions in the visibility of stars. Science, 379.
Li, X. & Li, D. (2014). Can night-time light images play a role in evaluating the Syrian crisis? IJRS, 35(18).
Li, X. et al. (2020). A harmonized global nighttime light dataset 1992–2018. Scientific Data, 7.
Martinez, L. R. (2022). How much should we trust the dictator’s GDP growth estimates? Journal of Political Economy, 130(10).
Román, M. O. et al. (2019). Satellite-based assessment of electricity restoration efforts in Puerto Rico after Hurricane Maria. PLOS ONE, 14(6).
Román, M. O. et al. (2018). NASA’s Black Marble nighttime lights product suite. Remote Sensing of Environment, 210.
Rural limits of conflict monitoring using nighttime lights (2025). Humanities and Social Sciences Communications.
IEA, IRENA, UN DESA, World Bank, WHO (2026). Tracking SDG 7: The Energy Progress Report.
DATA & TOOLS
NASA Black Marble
LAADS DAAC · Earthdata
Earth Observation Group
VNL composites, Nightfire
Google Earth Engine
Hosted, analysis-ready archive
HREA
Settlement electricity access
World Bank Open Nighttime Lights
Tutorials & notebooks
Notes: Leave this on screen during questions. For a five-minute first experiment, point people to the Radiance Light Trends web application or the World Bank Open Nighttime Lights tutorials before any heavy pipeline.